## Slide 1
OFFICE HOURS DISCUSSION
MXL Switcher
Open Core, live production proof
Eight live Zoom feeds, 2-up through 8-up Looks, and Companion control
Community roadmap · October 2026
Notes: Open with the result: this is a live working system, not a future architecture slide. Eight isolated Zoom participants enter one CPU-only node as native MXL flows. The node switches, composites, meters, monitors, and accepts browser or Companion control without another codec boundary between those production functions.
Keep the first minute visual. Show the multiview before explaining the architecture.

## Slide 2
The experiment found a viable boundary
Deterministic switching stays small while production capabilities remain replaceable
MEASURED ON THE ISOLATED SUPERMICRO PILOT
8h
loaded acceptance passed
2
independent NDI sources
0
media or timing faults
Switcher Core
Skins and control surfaces
Media functions and I/O
That boundary has survived real media, sustained load, and input-flow replacement.
Measured acceptance · Supermicro VM 101 · October 2026
02
Notes: The original diagnosis showed that the heavy work lived around the switcher. The new architecture isolates timing, source selection, stable Program and Preview flows, control, and health reporting.
Acceptance evidence now includes an eight-hour loaded run with one real NDI source and one synthetic v210 source, followed by a clean five-minute loaded run with two independent real NDI sources. Both sustained NDI outputs decoded with zero drops during the two-real-source gate.
Source:
- https://github.com/guycochran/mxl-switcher-core/blob/main/docs/ACCEPTANCE_2026-10-12.md

## Slide 3
The product boundary
A narrow Core gives the wider MXL ecosystem a dependable switching contract
MXL Switcher Core
A headless service that keeps Program and Preview deterministic inside MXL while control surfaces and media functions evolve independently.
BUILD HERE
Frame-boundary TAKE
Stable PGM and PVW flows
Adaptive frame synchronization
HTTP control and SSE tally
Per-source health attribution
REUSE ELSEWHERE
OBS scenes and graphics
Transport adapters and encoders
Replay, captions, and multiview
Operator control surfaces
Public prototype and tested contract
03
Notes: This boundary is now implemented in the public prototype. The Core performs deterministic frame-boundary TAKEs between configured native v210 sources, preserves stable Program and Preview flow identities, exposes HTTP control and SSE tally/state, and attributes media faults to the upstream source. Transitions, audio-follow-video, graphics, replay, multiview, and encoding remain outside the current Core.
Sources:
- https://github.com/guycochran/mxl-switcher-core

## Slide 4
Core, skin, and media function
These names separate operator experience, deterministic switching, and video processing
SKIN
Buttons, layouts, macros, tally, operator workflow
MXL CORE
Timing, source selection, stable flows, state, health
MEDIA FUNCTION
Graphics, replay, ingest, multiview, encode, transport
Control API
MXL flows
A Skin can disappear without interrupting media. A function can change without redesigning the switcher.
Proposed extension model
04
Notes: This terminology is important. A skin is a control surface only. Anything that processes or creates media is a media function. That keeps custom community interfaces easy to build while protecting the reliability of the media path.

## Slide 5
The MXL-native media path
v210 remains the canonical video format inside each production node
TRANSPORT I/O
NDI · SRT · SDI
WebRTC
MXL FLOW
v210 · Float32 · ANC
SWITCHER CORE
PGM · PVW
frame sync
OUTPUT FUNCTIONS
Encode · SDI
Stream · record
Decode once
Shared memory
Select and route
Encode once
OPERATING RULE
Transport and compression conversions happen at the edges. Local functions exchange native MXL grains.
MXL v1 operating point: progressive v210/v210a video, Float32 audio, ANC
05
Notes: The earlier suggestion to use NV12 as the canonical internal format was wrong for this product. The opportunity is to remove redundant conversions and transports around v210, not replace v210. NDI, SRT, SDI, and WebRTC belong at the edge, where an adapter converts them into native MXL flows. MXL-Lab demonstrates NDI ingest converted to v210 before mxlsink. A 1080p60 v210 flow is roughly 2.65 Gbit/s of payload, which makes same-host shared-memory placement important.
Sources:
- https://github.com/dmf-mxl/mxl
- https://github.com/dmf-mxl/mxl-requirements/blob/main/Initial-MXL-Requirements.md
- https://github.com/mykeman/MXL-Lab/blob/main/scripts/run-ingest.sh

## Slide 6
The OBS-MXL bridge already exists
Mathieu Rochon's public fork proves that OBS can consume and publish MXL flows
MXL source
MXL program output
rochonma/obs-mxl-plugin-latest
Public repository screenshots
06
Notes: Mathieu Rochon is a Senior Technical Advisor at CBC/Radio-Canada and a visible MXL/DMF contributor. His repository is a fork of JohannesItten/obs-mxl-plugin. The bridge proves OBS can participate as an MXL media function.
Sources:
- https://github.com/rochonma/obs-mxl-plugin-latest
- https://github.com/JohannesItten/obs-mxl-plugin
- https://tech.ebu.ch/news/2025/06/ebu-launches-open-source-mxl-sdk-for-software-based-media-exchange

## Slide 7
What the prototype has proved
The current evidence supports a community alpha while keeping important limits visible
CORE
Deterministic switching
Eight-hour loaded run
Stable PGM and PVW identities
Frame-boundary TAKE
Adaptive common-window timing
TRANSPORT
Real NDI input and output
Eight ZoomISO video flows
Native v210 video in MXL
Separate Float32 audio flows
RECOVERY
Reader reopen and held output
Per-source fault attribution
Short recovery tests passed
Long-switch recovery remains open
The media plane is credible. Audio content, multiview composition, encoded egress, and long-switch recovery still need proof.
Measured prototype · October 2026
07
Notes: Verified results now span both facility and meeting-media workflows:
- Eight-hour loaded Core acceptance passed with stable Program and Preview and no fatal media or timing faults.
- Two real NDI sources passed loaded switching and return-output tests.
- Four 1080p30 ZoomISO inputs passed a 30-minute local CPU-only confirmation.
- Eight 1080p29.97 ZoomISO video flows passed clean direct and Core gates on one CPU-only Azure VM.
Important limits:
- ZoomISO created separate Float32 audio flows, but active audio content still requires a controlled proof.
- A longer Azure switching run exposed a sustained-unavailable alarm during source reactivation. The alarm recovered and did not coincide with host saturation, but the recovery path remains open.
Sources:
- https://github.com/guycochran/mxl-switcher-core/blob/main/docs/ACCEPTANCE_2026-10-12.md
- https://github.com/guycochran/mxl-switcher-core/blob/main/docs/ZOOMISO_MXL_ACCEPTANCE_2026-10-12.md
- Internal Azure validation evidence, 2026-10-13

## Slide 8
Capability grows without enlarging the Core
Each layer has a clear job, test boundary, and replacement path
TRANSPORT I/O
NDI · SRT · SDI
MXL FABRIC
v210 · Float32
SWITCHER CORE
PGM · PVW
MEDIA FUNCTIONS
GFX · replay · MV
SKINS
web · panels · OBS
Convert at the edge
Share native media locally
The Core stays deterministic while the community adds production capability around it.
Proposed product architecture
08
Notes: The architectural rule is simple: transports own network behavior and format conversion; MXL owns native local exchange; the Core owns synchronized selection and stable Program/Preview identities; media functions own processing; Skins own the operator experience.

## Slide 9
The Big Plan
The next visible proof is a native compositor, followed by real output functions and portable hardware profiles
HORIZON | WHAT SHIPS | PROOF | WHO CAN HELP
Now | Reliable Core plus NDI and ZoomISO MXL paths | Eight-hour Core and eight-input gates | Operators and test owners
Next | Native compositor with 2-up through 8-up looks | Changing tiles, GFX tracking, zero output drops | Graphics and media developers
Then | Audio plus NDI, SRT, record, and stream outputs | AV sync, measured latency, eight-hour output gate | Audio and I/O developers
Later | AWS, GCP, Azure, and on-prem hardware profiles | Capacity and cost crossover on one harness | Cloud and facility engineers
Finish the native compositor first. Then every cloud and server comparison measures a useful production output, not an isolated ingest test.
Community roadmap
09
Notes: The architecture and ingest path now have enough evidence to move the visible production function to the front of the roadmap. The immediate community target is a native MXL compositor with repeatable 2-up through 8-up looks, followed by output adapters and cross-cloud sizing.
Keep audio and recovery limits visible. A feature moves into the passed column only after changing-content, cadence, drop, latency, and resource checks pass under load.

## Slide 10
Target architecture
One deterministic Core with replaceable control surfaces, I/O adapters, and media functions
MXL SWITCHER CORE
PGM · PVW · frame sync · state · health
Web skin
Hardware panel
Automation
OBS
scenes + GFX
Replay
Transport I/O
Multiview
HTTP + SSE
MXL flows
Skins use the control contract. Media functions exchange MXL flows. Neither owns the Core lifecycle.
Target platform boundary
10
Notes: The control and media sides have different contracts. The current Core exposes HTTP commands plus an SSE state/tally stream to skins and automation. It exchanges native v210 MXL flows with media functions. OBS is a candidate graphics and scene-composition function, not a required dependency.
Sources:
- https://github.com/guycochran/mxl-switcher-core

## Slide 11
Current live demo stack
The useful production path is working now; audience-return audio remains the next acceptance gate
PASSED
CORE + BUSES
Eight live 1080p inputs
Stable Program and Preview
Frame-boundary direct cuts
RUNNING
OPERATOR + LOOKS
ATEM-style browser Skin
Companion / Stream Deck
Warm ME A/B · 2-up through 8-up
VISIBLE OUTPUT
Confidence + audio
Program, Preview, and multiview WebRTC
Per-source VU meters
AFV and manual Program mixer
Tonight's proof: eight pictures in, deterministic cuts, off-air Look preparation, instant ME bank CUT, and two independent control surfaces.
Acceptance evidence · October 2026
11
Notes: Use this slide as the verbal checklist before the live switch.
Validated for the demonstration:
- Eight isolated 1920×1080p29.97 ZoomISO video inputs on a CPU-only Azure VM.
- Stable Program and Preview identities with frame-boundary direct cuts.
- Two persistent compositor banks with 2-up through 8-up Looks.
- Warm Look preparation in roughly 0.9–1.8 seconds while the on-air bank remains unchanged.
- Immediate CUT between prepared ME banks.
- Browser multiview and Companion/Stream Deck control with tally.
- Native 48 kHz Float32 source audio, meters, AFV/manual mixing, and a separate clock-correction candidate.
Do not claim that the audience-meeting return or end-to-end A/V sync is finished. The candidate is deliberately not mapped into the live show.

## Slide 12
Transport I/O at the facility edge
Adapters connect familiar network and hardware sources to native local MXL flows
TRANSPORT / MXL I/O
Receive, normalize, publish
NDI cameras
ZoomISO and SRT
OBS, SDI, tools
MXL Core
Graphics
Multiview
Record / stream
NDI network
Native MXL flows
Receive or decode once at the boundary. Core, graphics, multiview, and record functions share the native local flow.
First public I/O: NDI
12
Notes: Research finding: no purpose-built public NDI-to-MXL bridge was found in GitHub repository search or exact public code searches for the NDI SDK symbols together with MXL. The closest composable path is Teltek's Linux GStreamer NDI source/sink plus the gst-mxl-rs elements released with MXL 1.1.
Architectural recommendation: keep NDI outside MXL Switcher Core. A separate edge gateway owns NDI discovery, receive/decode, source reconnect, color conversion, audio mapping, and optional NDI return output. It publishes native v210 video and Float32 audio into MXL. The Core continues to select and route existing MXL flows without linking to the proprietary NDI SDK.
The benefit appears when several local functions need the same source. The node receives and decodes NDI once, then Core, graphics, multiview, record, and encode functions share the native timed flow through MXL. NDI remains useful for the facility network; MXL removes repeated network and codec boundaries among neighboring applications.
Sources:
- https://github.com/teltek/gst-plugin-ndi
- https://github.com/dmf-mxl/mxl/releases/tag/v1.1.0
- https://ndi.video/for-developers/ndi-sdk/
- https://docs.ndi.video/all/developing-with-ndi/sdk/ndi-recv
- GitHub public repository and code searches performed 2026-10-10

## Slide 13
From lab build to community alpha
A useful alpha works for someone other than the original developers
PACKAGE
Linux appliance
One-command deployment
Hardware and VM profiles
Preflight checks
Safe upgrade and rollback
CONTRACT
Core API
Source registration
PGM, PVW, TAKE, and tally
Health and authentication
Stable compatibility policy
FIRST SKIN
Operator Skin
Multiview and tally
Audio meters and source health
Keyboard, Stream Deck, MIDI
Stream and record controls
Alpha exit test: a community member deploys it on a fresh machine, switches a show, diagnoses a failure, and adds one integration.
Proposed community alpha
13
Notes: The alpha should optimize for repeatability and extension, not an exhaustive feature list. The first operator Skin proves the API and provides a useful demo, but it remains replaceable. Audio-follow-video belongs in the near-term media contract because a switcher without audio cannot support a complete show.

## Slide 14
ZoomISO Cloud makes the MXL case concrete
Eight isolated participant outputs entered one Azure production node as native MXL flows
ZOOM MEETING
remote participants
ZOOMISO CLOUD
8 × 1080p29.97
MXL FLOWS
video + Float32 audio
CORE + OUTPUTS
PGM · PVW · next compositor
Join
Eight participant flows
Share locally
Switch and compose
MEASURED THIS WEEK
One modern CPU-only cloud VM sustained eight ZoomISO outputs and two Core outputs during clean 10-minute gates.
Azure D32s v5 · no GPU · audio silence and long-switch recovery remain open investigations
14
Notes: Measured result, 2026-10-13:
- ZoomISO Cloud 0.1.0.77 published eight 1920×1080 participant video flows at 30000/1001 plus eight separate Float32 stereo audio flows.
- A direct 10-minute gate passed with all eight pictures changing and all eight audio flows advancing at approximately 48 kHz.
- The 10-minute Core confirmation produced stable Program and Preview at 29.97 fps with zero output drops and no fatal timing-counter movement.
- ZoomISO averaged approximately 438% CPU on a 32-vCPU Azure D32s v5 host. Core averaged approximately 15% of one CPU. No GPU was present or required.
Important limits:
- The native log showed that ZoomISO writes silence whenever converted Zoom audio misses its MXL deadline. A controlled active-audio test is still required.
- A later 30-minute switching gate stopped when the candidate Core raised sustained-unavailable alarms during source reactivation. The alarms recovered, and the incident did not coincide with host saturation. This remains a Core recovery issue, not an eight-output capacity result.
Sources:
- Microsoft Azure Linux VM benchmark table for Dsv5: https://learn.microsoft.com/en-us/azure/virtual-machines/linux/compute-benchmark-scores
- Internal Azure validation evidence, 2026-10-13

## Slide 15
Why MXL is worth stopping for
The payoff compounds as one native media plane serves more production functions on the same node
FEWER CODEC BOUNDARIES
Ingest once
Switch, compose, meter, monitor, record, and encode from the same timed native media.
LIVE, MODULAR OPERATIONS
Change one function
Stable flows keep Program alive while a Skin, compositor, or output adapter changes independently.
OPEN CONTROL + OUTPUTS
Use the right surface
Browser, Companion, or automation control the same Core; one Program Master can feed many adapters.
Proven live: eight 1080p Zoom feeds, direct cuts, 2-up through 8-up Looks, multiview, VU meters, and Stream Deck control on a CPU-only node.
Tonight's reason to care
15
Notes: This is the attention slide. Lead with what the audience can see tonight, then explain why it matters.
1. MXL removes repeated codec and transport boundaries between neighboring applications on one node.
2. Stable native flows let small applications do one job well and be replaced independently.
3. The same media can serve switching, composition, monitoring, graphics, recording, and egress.
4. The operator is not locked to one UI: browser, Companion, and automation share the control contract.
5. The proof runs on CPUs only. The local older server and the modern Azure VM show a path from inexpensive lab hardware to cloud production.
The honest limit: this is strong architectural and capability evidence, not yet a matched MXL-versus-NDI cost benchmark.
Source:
- https://github.com/dmf-mxl/mxl

## Slide 16
The efficiency case now has measured evidence
An older on-premises server and a modern cloud VM both carried native MXL workflows without GPU acceleration
MEASURED 1080p WORKFLOWS
4
local ZoomISO inputs
8
Azure ZoomISO inputs
0
GPUs required
LOCAL
Dual E5-2630L v3
30-minute four-input gate
AZURE
D32s v5
10-minute eight-input gate
NEXT
Right-size CPU profiles
Add real output functions
The result supports the architecture. The next proof must compare equivalent complete workflows, including multiview and encoded egress.
Measured capacity · not yet a cloud-cost benchmark
16
Notes: Local evidence:
- The Supermicro host uses two Intel Xeon E5-2630L v3 processors: 16 physical cores and 32 threads in total, with a 1.80 GHz base frequency.
- A 30-minute four-input ZoomISO MXL 1920×1080p30 confirmation passed. The Core, Program, Preview, and input probes stayed healthy with zero output drops.
- ZoomISO used 268.58–839.35% CPU during the confirmation. The workload did not depend on the installed GPU.
Azure evidence:
- One ZoomISO instance published eight 1920×1080p29.97 participant outputs on a Standard_D32s_v5 VM.
- The direct 10-minute gate and the 10-minute Core gate passed. ZoomISO averaged approximately 438% CPU and the Core approximately 15% of one CPU.
- This is strong capacity evidence, but the VM was intentionally oversized. It does not yet establish the minimum cloud size or cost advantage.
The 30-minute Core switching attempt exposed a source-reactivation alarm after the clean 10-minute result. Keep that software-recovery issue separate from the host-capacity conclusion.
Sources:
- https://github.com/guycochran/mxl-switcher-core/blob/main/docs/ZOOMISO_MXL_ACCEPTANCE_2026-10-12.md
- https://learn.microsoft.com/en-us/azure/virtual-machines/linux/compute-benchmark-scores
- Internal Azure validation evidence, 2026-10-13

## Slide 17
A practical Supermicro upgrade path
The dual-socket platform may reach 40 physical cores, but board, BIOS, power, and cooling checks come first
CURRENT
Two E5-2630L v3 CPUs
16 cores and 32 threads
1.80 GHz base, 2.90 GHz turbo
55 W per socket
Known working baseline
CANDIDATE
Two E5-2698 v4 CPUs
40 cores and 80 threads
2.20 GHz base, 3.60 GHz turbo
135 W per socket
Same dual-socket processor family
GO OR NO-GO
Verify the chassis
Exact motherboard model
Current BIOS and v4 CPU support
Heatsinks, airflow, and PSU margin
Then repeat four- and eight-output gates
Likely useful as a low-cost lab upgrade. Newer CPUs may still win when a workload depends on a few fast threads rather than total core count.
Conditional hardware recommendation
17
Notes: The current diagnostics confirm a dual-socket E5-2600 v3 platform, but they do not contain the exact Supermicro motherboard model. Many dual-socket Supermicro X10 platforms support E5-2600 v4 processors after an appropriate BIOS update, but that must be verified against the exact board revision and BIOS release before purchasing CPUs.
Two E5-2698 v4 processors would provide 40 physical cores and 80 threads. Compared with the current pair, the upgrade also raises base and turbo frequency, but it increases CPU TDP from 55 W to 135 W per socket. Cooling, power delivery, and fan profiles therefore matter.
This upgrade should be treated as an inexpensive capacity experiment, not proof that old 40-core hardware equals a modern cloud CPU. The benchmark must record both total throughput and single-thread saturation.
Sources:
- Intel E5-2630L v3 specifications: https://www.intel.com/content/www/us/en/products/sku/83357/intel-xeon-processor-e52630l-v3-20m-cache-1-80-ghz/specifications.html
- Intel E5-2698 v4 specifications: https://www.intel.com/content/www/us/en/products/sku/91753/intel-xeon-processor-e52698-v4-50m-cache-2-20-ghz/specifications.html
- Local read-only Supermicro diagnostics, 2026-10-10

## Slide 18
One Program Master, many output adapters
Keep switching and composition native; convert only at the destination boundary
ONE MXL PRODUCTION NODE
8 inputs · Core · warm ME A/B · Program Master
INPUT
ZoomISO / NDI
CORE
PGM + PVW
COMPOSE
2-up to 8-up
Zoom meeting return
WebRTC confidence
NDI · SRT · SDI
RTMP · record
Stable Program identity
Isolated adapters
Each adapter owns its codec, transport, reconnect, and latency policy. A failed destination must not recreate Program or interrupt another output.
Output architecture
18
Notes: WebRTC confidence is visible in the live system. The remaining destinations are the adapter roadmap, not claims of completed integrations.
The contract is one stable MXL Program Master with paired video and exact-48-kHz audio. Meeting return, NDI, SRT, SDI, recording, and RTMP are independent consumers. This preserves fault containment and lets each edge use the protocol and codec it actually needs.
The isolated audio candidate has already demonstrated clock measurement, bounded correction, exact-48-kHz output pacing, zero output PTS discontinuities, and zero hard sample corrections during a clean live trace. It remains outside tonight's default meeting-return mapping until the end-to-end A/V gate passes.

## Slide 19
Tonight's demo ladder
Each step proves one claim and has a no-drama fallback
STAGE | SHOW IT | PROOF | FALLBACK
1 | Eight-source 4×2 multiview | All inputs are live and independently selectable | Cut directly to input 1
2 | Preview 1–8, then CUT | Stable PGM/PVW plus browser and Companion tally | Operate only from Companion
3 | 2-up, 4-up, then 8-up | Off-air ME preparation and immediate bank CUT | Return to known-good 2-up
4 | Program confidence and VU meters | Visible output plus native audio presence | Mute browser audio; explain next gate
End on a direct source in Program and a prepared composition in Preview. Do not restart ZoomISO, Core, or a live ME bank during the session.
Eight-to-ten-minute run of show
19
Notes: Run the read-only preflight immediately before the session. Do not attach deep MXL probes during the show; a non-dropping diagnostic reader can backpressure a small audio ring.
Suggested pacing:
- 45 seconds: frame the native-media point.
- 60 seconds: prove all eight sources.
- 90 seconds: direct cuts and tally.
- Three minutes: 2-up, 4-up, and 8-up through the inactive ME bank.
- 60 seconds: browser versus Companion control.
- 60 seconds: Program Master output architecture.
- 30 seconds: close on one media plane, many useful functions.

## Slide 20
Seven- and eight-picture looks
Side-by-side PiPs stay visually simple while each source keeps an attached graphics strip
7-UP LOOK · FOUR PLUS THREE
CAM 1
NAME 1
CAM 2
NAME 2
CAM 3
NAME 3
CAM 4
NAME 4
CAM 5
NAME 5
CAM 6
NAME 6
CAM 7
NAME 7
8-UP LOOK · FOUR BY TWO
CAM 1
NAME 1
CAM 2
NAME 2
CAM 3
NAME 3
CAM 4
NAME 4
CAM 5
NAME 5
CAM 6
NAME 6
CAM 7
NAME 7
CAM 8
NAME 8
Every tile must keep changing, every GFX strip must follow its source, and the 1080p output must hold cadence with zero drops.
Proposed multiview looks
20
Notes: These are production-oriented looks, not only engineering multiview grids. Each participant tile has a dedicated graphics strip for a name, role, score, topic, or sponsor treatment.
The 7-up layout uses four tiles on the first row and three centered on the second. The 8-up layout uses a 4×2 grid. Both should be tested with changing content in every tile, live graphics updates, source swaps, Program/Preview routing, and a clean 1080p29.97 or 1080p30 output.
After the native MXL output passes, repeat the chosen look with NDI, SRT, recording, or streaming egress.

## Slide 21
Who wants to play?
The new Office Hours Discord channel can turn the roadmap into shared experiments
01
Where would a small MXL-native switching Core help your production?
02
Which useful output should attach to Program Master first: Zoom, NDI, SRT, SDI, record, or RTMP?
03
Who wants to turn one of tonight's 2-up through 8-up Looks into a reusable production template?
04
Would you build a Skin, media function, transport adapter, or OBS bridge?
05
What matched benchmark would convince you that fewer internal codec boundaries matter?
Join the channel. Bring a source, a destination, a control surface, a machine, or code.
github.com/guycochran/mxl-switcher-core
21
Notes: Invite concrete participation. The Core, Skin, Companion module, multiview, and compositor are tangible integration surfaces. The next high-value contribution is a destination adapter or a matched capacity benchmark.
Public code:
- https://github.com/guycochran/mxl-switcher-core
- https://github.com/guycochran/MXL-Lab/tree/codex/ndi-core-ingress